## Slide 1: Chapter 5 Network and Transport Layers
Part 2

## Slide 2: Chapter 5 Outline
Transport & Network Layer Protocols
  TCP/IP
Transport Layer Functions
  Linking to the Application Layer
  Segmenting
  Session management
Addressing
  Assigning addresses and address resolution
Routing
  Types of routing, routing protocols, and multicasting
TCP/IP Examples
Copyright 2010
John Wiley & Sons, Inc

## Slide 3: Network Layers
Computer 1
Computer 2

## Slide 4: Transport Layer Functions
Segmenting
Linking to the Application Layer
Session management
  Connection-oriented
  Connectionless
  Quality of Service (QoS)
Transport Layer
Application Layer
Network Layer

## Slide 5: 5.2.3.1 Session Management - Connection Oriented
Setting up a virtual circuit, or a TCP connection
  Packet deliveries are acknowledged
For which application layer packets does the transport layer use a connection oriented session for?

## Slide 6: 5.2.3.2 Session Management - Connectionless Routing
Provided by UDP
  Sending packets individually without a virtual circuit
  Each packet is sent independently of one another, and will be routed separately, following different routes and arriving at different times
For which application layer packets does the transport layer use a connection oriented session for?

## Slide 7: 5.2.3.2 UDP - User Datagram Protocol
Protocol used for connectionless routing in TCP/IP suite that uses no acks, no flow control
Uses only a small packet header
  Only 8 bytes containing only 4 fields:
    Source port
    Destination port
    Message length
    Header checksum
Can also be used for applications where a packet can be lost, such as information rich video

## Slide 8: 5.2.3.3 Protocols Supporting QoS
Asynchronous Transfer Mode (ATM)
  A high-speed data link layer protocol
TCP/IP protocol suite
  Resource Reservation Protocol (RSVP)
    Sets up virtual circuits for general purpose real-time applications
  Real-Time Streaming Protocol (RTSP)
    Sets up virtual circuits for audio-video
    applications
  Real-Time Transport Protocol (RTP)
    Used after a virtual connection setup by RSVP or RTSP
    Adds a sequence number and a timestamp for helping applications to synchronize delivery
    Uses UDP (because of its small header) as transport
IP
RTSP
RSVP
UDP
RTP

## Slide 9: Network Layer Functions
Addressing
  Each device on the path between source and destination must have an address
  Internet Addresses
  Assignment of addresses
  Translation between network layer
  addresses and other addresses
  (address resolution)
Routing
  Process of deciding what path a packet must take to reach destination
  Routing protocols
Network Layer
Transport Layer
Data Link Layer

## Slide 10: 5.3.1 Types of Addresses
Application Layer Address
Network Layer Address
Data Link Layer Address
Network Layer
Data Link Layer
Application Layer
Transport Layer

## Slide 11: 5.3.1 Types of Addresses
Address Type
Example
Example Address
Application Layer
Network Layer
Data Link Layer
IP address
URL
MAC address
www.iub.edu
129.79.127.4 (4 bytes)
00-0C-00-F5-03-5A
(6 bytes)
Name
Zip code
Street
address
Analogy
These addresses must be translated from one type to another for a message to travel from sender to receiver.
This translation process is called address resolution.

## Slide 12: 5.3.1 Question: Addresses and Clients
How many addresses are assigned to the different computers in this room?
  Desktop
  Laptop

## Slide 13: 5.3.2 Assignment of Addresses
Data Link Layer Address (MAC address)
  Unique hardware addresses placed on network interface cards by their manufacturers ( based on a standardized scheme)
How are these set?
What do you they look like?
http://www.coffer.com/mac_find/

## Slide 14: 5.3.2 Assignment of Addresses
Application Layer address (URL)
  For servers only (clients don’t need it)
  Assigned by network managers and placed in configuration files.
  Some servers may have several application layer addresses
Network Layer Address (IP address)
  Assigned by network managers, or by programs such as DHCP, and placed in configuration files
  Every network on the Internet is assigned a range of possible IP addresses for use on its network

## Slide 15: 5.3.2 Internet Addresses
Managed by ICANN
  Internet Corporation for Assigned Names and Numbers
  Manages the assignment of both IP and application layer name space (domain names)
    Both assigned at the same time and in groups
    Manages some domains directly (e.g., .com, .org, .net) and
    Authorizes private companies to become domain name registrars as well
Example: UNCW
  URL that end in .uncw.edu
  IP addresses in the 152.20.x.x range (where x is any number between 0 and 255)

## Slide 16: 5.3.2 How do you decide who gets what address?
Group of computers on the same LAN with IP numbers using the same prefix
Assigned addresses
  For example:
    Subnet 152.20.234.x
      Computers in CIS labs (x is between 0 & 255)
    Subnet 152.20.244.x & 152.20.196.x
      Computers in CIS Offices (x is between 0 & 255)
    Subnet 129.79.125.x
      Computers in Cameron
Does anyone see a problem with the subnets above?

## Slide 17: 5.3.2 Subnets: Example

## Slide 18: 5.3.2 Subnets
How do you think UNCW handles assigning address?
How does the server know where to send the IP address if it doesn’t have one?

## Slide 19: 5.3.2 Dynamic Addressing
Giving addresses to clients (automatically) only when they are logged in to a network
Uses a server to supply IP addresses to computers whenever the computers connect to network

## Slide 20: 5.3.2 Programs for Dynamic Addressing
Protocols:
  Bootstrap Protocol (bootp)
  Dynamic Host Control Protocol (DHCP)
Different approaches, but same basic operations:

## Slide 21: 5.3.3 Address Resolution
Server Name Resolution
Data Link Layer Address Resolution

## Slide 22: 5.3.3 Server Name Resolution - DNS
Used to determine IP address for a given URL
Provided through a group of name servers
  Databases containing directories of domain names and their corresponding IP addresses
Large organizations maintain their own name servers
  smaller organizations rely on name servers provided by their ISPs
When a domain name is registered, IP address of the DNS server must be provided to registrar for all URLs in this domain
  Example: Domain name: uncw.edu
  URLs: www.uncw.edu, csb.uncw.edu, www.uncw.edu/cas/index.html

## Slide 23: 5.3.3 How DNS Works – Directory Service
Where are address tables located?

## Slide 24: 5.3.3 How DNS Works (Cont.)
If the URL is NOT in the local DNS server
  Sends DNS request packet to the next highest name server in the DNS hierarchy
  Usually the DNS server at the top level domain (such as the DNS server for all .edu domains)
  If the URL is NOT in the name server
    Sends DNS request packet ahead to name server at the next lower level of the DNS hierarchy

## Slide 25: 5.3.3 DNS Hierarchy

## Slide 26: 5.3.3 DNS Hierarchy
http://www.root-servers.org/

## Slide 27: 5.3.3 How DNS Works – Internal Request

## Slide 28: 5.3.3 How DNS Works – External Request

## Slide 29: 5.3.4 MAC Address Resolution
Problem: Unknown MAC address of the next node (whose IP address is known)
Solution:
Operation: